## Slide 1: Approximating Warps with Intra-warp Operand Value Similarity
Daniel Wong†, Nam Sung Kim‡, Murali Annavaram¥
†University of California, Riverside dwong@ece.ucr.edu
‡University of Illinois, Urbana-Champagin
¥University of Southern California

## Slide 2: Value Similarity
Values differ only in the least significant bits
d-similar
  Values that differ in the d least significant bits
113 11100012
127 11111112
4-similar

## Slide 3: Intra-warp Operand Value Similarity
Warp consists of 32 threads
  Each thread execute same instruction
  on it’s own data
Intra-warp operand value similarity
  input operands of all threads within a warp exhibit value similarity
Warp
  
ADD
8 6
10 5
9 4
8, 10, 9 2-similar
6, 5, 4 2-similar

## Slide 4: Significant Value Similarity Exists
Significant value similarity exists even with low d-similarity levels

## Slide 5: How can we leverage value similarity for approximate computing?

## Slide 6: Warp Approximation
14
15
13
Warp
  
ADD
8 6
10 5
9 4

## Slide 7: Warp Approximation
14
Warp
  
ADD
8 6
10 5
9 4

## Slide 8: Warp Approximation
Coarse-grain Annotation
Identify Operand Value Similarity
≈
Representative Value Storage

Representative Thread Execution

## Slide 9: Coarse-grain Annotation
Identify regions of code where approximation can be tolerated, and opportunistically approximate when hardware detects value similarity
API / ISA extension
  Start / End of approximable region
    Sets per warp ApproxBit in hardware
  Level of approximation
Programmer / Compiler annotate coarse-grain approximable regions

## Slide 10: Programmer Support

## Slide 11: Warp Approximation
Coarse-grain Annotation
Identify Operand Value Similarity
≈
Representative Value Storage

Representative Thread Execution

## Slide 12: Detecting value similarity
Add value similarity detection stages before Write-back stage to Register File
≈

## Slide 13: Detecting value similarity
Comparison selection stage to select value from active thread
≈

## Slide 14: Detecting value similarity
Comparison stage checks for value similarity
SimilarBit set if value similarity exist
≈

## Slide 15: Warp Approximation
Coarse-grain Annotation
Identify Operand Value Similarity
≈
Representative Value Storage

Representative Thread Execution

## Slide 16: Representative Value Storage
Instead of storing entire vector register entry, store a value similar scalar, called the representative value.
Reduce access energy for reading/writing representative value to register file
Representative value is picked from a Representative Thread

## Slide 17: Selecting Representative Thread
Pick lowest order lane
RT Selector logic is simply a priority encoder and decoder
Representative Thread Mask (RT Mask)
  1 for representative thread
  0 for all other threads

## Slide 18: Writing Representative Values
1
8 |  |  |  | 
8 | 10 | … | … | 9
SimilarBit
1 | 0 | … | ... | 0
RT Mask
≈

## Slide 19: Handling Divergence
0 | 1 | … | ... | 0
0
8 | 10 | … | … | 9
A/11…1
B/10…1
C/01…0
1
8 |  |  |  | 
SimilarBit
1 | 0 | … | ... | 0
RT Mask
✓
✗
9 |  |  |  | 
Need to copy representative value on divergence
Basic Block/ Active Mask

## Slide 20: Handling Divergence
On divergence, copy representative value using dummy MOV instruction†
Supports only 1 level of divergence
On convergence or nested divergence, expand representative values
†Sangpil Lee, et. al. Warped-compression: enabling power efficient GPUs through register compression. In ISCA’15

## Slide 21: Handling Divergence
8 |  |  |  | 
8 | 8 |  |  | 
9 | 8 |  |  | 
0 | 1 | … | ... | 0
A/11…1
B/10…1
C/01…0
SimilarBit
1 | 0 | … | ... | 0
RT Mask
✓
✓
1
9 | 10 |  |  | 
Basic Block/ Active Mask

## Slide 22: Handling Divergence
Basic Block/ Active Mask
A/11…1
B/10…1
C/01…0
SimilarBit
1
D/11…1
9 | 10 |  |  | 
On convergence, expand each representative value w/ active mask
9 | 10 | … | … | 9
0

## Slide 23: Warp Approximation
Coarse-grain Annotation
Identify Operand Value Similarity
≈
Representative Value Storage

Representative Thread Execution

## Slide 24: Representative Thread Execution
Instead of executing all lanes in a warp precisely, we pick a single representative thread to execute
Executing a single lane reduces dynamic energy
Idle lanes can be power gated to reduce static energy†

†Mohammad Abdel-Majeed, et. al. Warped gates: gating aware scheduling and power gating for GPGPUs. In MICRO’13
Qiumin Xu and Murali Annavaram. PATS: pattern aware scheduling and power gating for GPGPUs. In PACT’14

## Slide 25: Representative Thread Execution
Simply use RT Mask as Active Mask
If some input operands are not similar, and others are, then we need to expand the representative value read from the RF using broadcast logic


## Slide 26: Warp Approximation
Coarse-grain Annotation
Identify Operand Value Similarity
≈
Representative Value Storage

Representative Thread Execution

## Slide 27: EVALUATION

## Slide 28: Methodology
GPGPU-Sim v3.2.1
  Nvidia GTX480-like architecture
GPUWattch + McPAT
Lane-level Power Gating†
Benchmarks:
†Qiumin Xu and Murali Annavaram. PATS: pattern aware scheduling and power gating for GPGPUs. In PACT’14

## Slide 29: Application Error
Average error: 1.75%, Range: 0.006% - 5.5%
* Blackscholes d-similarity scaled by 2x

## Slide 30: Performance
Evaluated with various Warp Schedulers
  Round Robin, Two-level, Greedy-then-oldest
Negligible performance impact, regardless of warp scheduler

## Slide 31: Execution Unit Energy
Compared with lane power gating† and scalar execution units‡
†Qiumin Xu and Murali Annavaram. PATS: pattern aware scheduling and power gating for GPGPUs. In PACT’14 ‡Syed Zohaib Gilani, Nam Sung Kim, and Michael J. Schulte. Power-efficient computing for compute-intensive GPGPU applications. In PACT '12

## Slide 32: Register File Energy
Compared with Clock Gating (Base) and Scalar register files†
Warp Approximation creates more opportunities to reduce read/write access energy
†Syed Zohaib Gilani, Nam Sung Kim, and Michael J. Schulte. Power-efficient computing for compute-intensive GPGPU applications. In PACT '12

## Slide 33: Energy Efficiency
Energy efficiency = IPC/W
Efficiency related to amount of approximation opportunities
Average 26% improvement to energy efficiency

## Slide 34: Overheads
Assuming 45nm technology
Comparison logic
  12.75mW dynamic, 95.83uW leakage, 0.017mm2
Representative Thread selection and Broadcast
  19.76mW dynamic, 127.80uW leakage, 0.031mm2
Total overheads:
  1.7% dynamic energy
  0.0013% leakage energy
  0.098% area per SM

## Slide 35: More in paper
Optimizations
More evaluations
Discussion on error bounding

## Slide 36: Conclusion
Identify regions of code where approximation can be tolerated, and opportunistically approximate when hardware detects value similarity
Warp Approximation
=
Representative Value Storage
+
Representative Thread Execution
Improve energy efficiency by 26% with less than 5.5% error (on average 1.75%)


## Slide 37: Questions?
Thank you!